# Cartesian/Polar Grid Pattern Matching
Options:
1. Search parameter space of (grid line count, grid line start, grid line number, angle) for X and Y separately, while performing fast cross correlations using FFTW3.
2. Scan the X histogram vertically from top to bottom, and stopping when the existing points no longer fit the pattern FOREGROUND = START + (I – 1) * STEP

Option 1 took very long (30 seconds) to perform X then Y searches. Like most global peak searches, there were plenty of local peaks to interfere with performing gradient, and other, search optimizations.
Conclusion – Careful examination of various polar plots shows that the use of concentric rings as gridlines has little correlation with the plot type in terms of cartesian or polar. So cartesian/polar plot identification coding was stopped, and the files put into the deprecated subdirectory.
# Tutorial Video
Originally the tutorial video was to be added to the qrc file, but that caused a segfault on a 9MB file. Google search revealed adding large multimedia file(s) to resource file causes problems (since data gets stored as C array, and there are swap issues).
An attempt was made to play the mp4 file using Qt, by appending “multimedia multimediaplugins” to QT in the project file. This failed with an error that should have been fixed by installing libgstreamers. Playback using Qt was abandoned as too complicated and fragile to try to implement on many different platforms.
# Help Engine
1. Installed qttools5-dev and qttools-dev-tools in muon
2. 'build' script in help subdirectory builds the help files for the engauge executable. If the help files are not built, selecting Help / Help menu option brings up an empty Help dialog.